## Slide 1: Application Acceleration with High-Level Synthesis – Lab A (Interface synthesis)
111061545 陳揚哲

## Slide 2: Lab A (Interface synthesis)
Lab 1 Block-Level Protocol
Lab 2 Port-Level Protocol
Lab 3 Array Interface
Lab 4 AXI Interface

## Slide 3: Lab 1 (Block-level Protocol)
The block-level I/O protocol control RTL design by the control signal. (Independent of data I/O ports)
The block-level control ports contain ap_start, ap_ready, ap_done, ap_idle, and ap_continue.

## Slide 5: ap_ctrl_hs

## Slide 6: ap_ctrl_chain

## Slide 7: ap_ctrl_none

## Slide 8: Error in Co-simulation with ap_ctrl_none
Co-simulation requires a block-level I/O protocol to sequence the test bench.
The ap_ctrl_none doesn’t add the block level I/O ports. It can’t operate co-simulation.
However, in our case, this is the combinational logic, so we can operate co-simulation.

## Slide 9: Lab 2 (Port-level protocol)
The port-level I/O protocol is the data flow I/O ports.
There’re three different kinds port-level protocol.

## Slide 11: Set In1=ap_vld, In2=ap_ack, out1=ap_hs

## Slide 12
Notes: 1. The data on port in1 is only read when port in1_ap_vld is active-High.
2. Port in2_ap_ack will be active-High when data port in2 is read.
3. inout_i associated input valid port inout1_i_ap_vld and output acknowledge port inout1_i_ap_ack.
4. inout_o associated output valid port inout1_o_ap_vld and input acknowledge port inout1_o_ap_ack.

## Slide 13: Lab 3 (Array Interface)
This lab specifies implement different type of RTL port for array arguments.
If we use two-port RAM interface, this design can accept input data at twice rate of single port. Therefore, the estimated time of two port are lower.

## Slide 14
Solution 1 : Single port
(Type = Block)
Solution 2 : Two port Unroll (Type = Block)

## Slide 15: What if apply in rolled loop.
In rolled loop, loop is executed in turn.
This implementation code limits the logic to one read on d_i in each iteration.
In other word, reading d_i once in each loop. Thus, the estimated time wouldn’t be faster (solution5).

## Slide 16
Solution 1 : Single port (Type = Block)
Solution 2 : Two port unroll (Type = Block)
Solution 5 : Two port rolled (Type = Block)

## Slide 17: Array Partition
The input d_i will separate into the numbers of array partition factor RAM interfaces.
The output d_o will be divided into the numbers of array partition FIFO interfaces.
In this lab, we divide d_i into 2 seperated RAM interfaces and d_o into 4 FIFO interfaces. We also divide d_i and d_o completely.

## Slide 19
Solution 3:
d_i = 2, d_o = 4
Solution 6:
d_i = 2, d_o = 2
Solution 8:
d_i = 4, d_o = 4
Solution 9:
d_i = 4, d_o = 2
Solution 4:
complete
Notes: If we change the factor of d_i and d_o. we should first know the d_i = 2, d_o =4 means there’re two separate two port ram. If we change into d_i = 2, d_o
=2 or d_i = 4, d_o =4. These situations only have the single port interface. Further, if we set the d_o = 4, it means the output port only output 4 values at once. Thus, it’s no benefit for reading inputs higher than 4.

## Slide 20: Block v.s. Cyclic
For cyclic type, the smaller arrays are generated by interleaving elements from original array.
In this lab, the cyclic type is faster than block type.

## Slide 22: Lab 4 (AXI Interface)
In this lab, we set the interface as AXI4-stream.
We separate the d_o = 8 and d_i = 8 in axis protocol (AXI4-stream).
Compared to lab2, we can observe the data separation.

## Slide 24: Block-level interface signals
The hw.h file shows the addresses to access and control the block-level interface signals.
It shows how host program control the Axilite.

## Slide 25
For instance, if the bit 0 is set to value 1. The ap_start will be enabled.